## Slide 1: PCEP Extensions for Segment Routing leveraging the IPv6 data plane
draft-negi-pce-segment-routing-ipv6-00
Mahendra Singh Negi | Huawei
Prejeeth Kaladharan | 
Dhruv Dhody | 
Siva Sivabalan | Cisco

## Slide 2: Introduction & Motivation
Segment Routing (SR) can be used to steer packets through an IPv6 or MPLS network using the source routing paradigm.
Since SR can be applied to both MPLS and IPv6 data plane
  Should a PCE be able to compute SR-Path for both MPLS and IPv6 forwarding plane?
  And thus should PCEP be able to do this?

## Slide 3: PCEP for SRv6
Segment Routing can be applied to the IPv6 the Segment Routing Header (SRH).
  Segment identified by an IPv6 address
  Making it an ordered list of IPv6 addresses in the routing header
This document extends [I-D.ietf-pce-segment-routing] to support SR for IPv6 data plane.
  Extend SR-ERO, SR-RRO subobjects for SRv6
  Capability advertisement for SRv6 in PCEP
  A new path setup type

## Slide 4: PCEP Messages
No change here, all messages remains the same –
  PCReq
  PCRep
  PCRpt
  PCUpd
  PCInitiate
Only,
  The ERO object will use SR-ERO sub-object extended for SRv6
  The RRO object will use SR-RRO sub-object extended for SRv6

## Slide 5: PCEP Extn
SRv6-PCE-CAPABILITY TLV in OPEN
A new PST value for SRv6, carried in PATH-SETUP-TYPE TLV in RP/SRP object
SR-ERO Sub-object extended
  a new SID Type (ST)
  SRv6 Identifier (SRv6I) is the 128 bit IPv6 addresses representing SRv6 segment.
  SRv6ST indicates NAI
  Fn Code indicates function associated with SRv6 SID
  NAI - IPv6 Node ID or IPv6 Adjacency (optional)

## Slide 6: Next Steps
With this draft, we are making sure that the PCE and the PCEP can be used for both modes of SR
  Straight forward extension to existing SR work in PCEP
What does the WG think?
Comments?