## Slide 1: Generic PCEP Association & Protection Association Type
draft-ietf-pce-association-group-04
draft-ananthakrishnan-pce-stateful-path-protection-04
Ina Minei | Edward Crabbe | Siva Sivabalan | Hariharan Ananthakrishnan | Dhruv Dhody | Yosuke Tanaka | Colby Barth | Raveendra Torvi

## Slide 2: Association WG draft
draft-ietf-pce-association-group-04
  -03 was presented in IETF 99 remotely
A generic mechanism to create a grouping of LSPs in the context of a PCE.
  ASSOCIATION Object is defined for this purpose.
  Support for Dynamic Association (protection) as well as Operator-Configured Associations (policy)
IANA early code-point allocation was done!
  Thanks Chairs, AD

## Slide 3: Association Types
Generic Association
Diversity
Policy
Individual
Protection
Bidirectional
Resource Sharing
VN Association
MBB
Multi-Layer
WG
draft-ietf-pce-association-group-04
draft-ietf-pce-association-diversity-02
draft-ietf-pce-association-policy-01
draft-ananthakrishnan-pce-stateful-path-protection-04
draft-barth-pce-association-bidir-03
draft-zhang-pce-resource-sharing-05
draft-leedhody-pce-vn-association-03
draft-tanaka-pce-stateful-pce-mbb-04
draft-xiong-pce-multilayer-lsp-association-01
On the agenda today!
Generic Association is useful and ready for WG LC!

## Slide 4: Protection Association Draft
draft-ananthakrishnan-pce-stateful-path-protection-04
The very first association type that was originally published in June 2014
  along with generic association draft
-01 version was last discussed during IETF 95 (Buenos Aires)
What: PCEP extension to associate 2 or more LSPs to provide path protection!
How: Define “Path Protection Association Type” and re-use ASSOCIATION object.
  Path Protection Association Group (PPAG)
  Path Protection Association TLV where flags are defined
    P (PROTECTION-LSP) - Working or protection LSP
    S (STANDBY) - standby mode (protection LSP established prior to the failure)

## Slide 5: Update Since -01
Text around ‘dynamic association’ as per draft-ietf-pce-association-group-04
Error Handling text
  The endpoints and Tunnel ID MUST be same for all LSPs in the association group
Procedures for various Stateful PCE operations
Security and Manageability Considerations
Editorial changes to make text aligned to other documents
WG Adoption?
  Useful feature
  Draft has been stable and a good base for the WG
  Known Implementation