## Slide 1: draft-litkowski-pce-state-sync-02
Stephane Litkowski
Siva Sivabalan
Dhruv Dhody
State Synchronization Between Stateful PCE

## Slide 2: Introduction
Procedure for Inter-Stateful PCE communications
  Making PCE deployments more resilient
  Solve computation loop/optimality issues for dependent path computations (for e.g. diversity)
Work for all PCE-PCE relationships
  Redundant PCEs (backup or load-balance)
  Inter-domain PCEs
  Hierarchy of PCEs
Discussed previously in IETF 98 & 97

## Slide 3: Introduction
Generic procedures for the stateful inter-PCE communication
  A state-sync PCEP session between Stateful PCEs
  Bi-directional state synchronization between stateful PCEs
  Master-Slave relationship between PCEs for a group of LSPs
    PCE election based on priority (how the priority is set/advertised is out of scope)
  A set of forwarding rules of LSP state
  Sub-delegation procedures

## Slide 4: Updates in -02
How to make sure the “latest” state is synchronized at PCEs in case of learning LSP state from multiple sources?
  A single “freshest” state for the LSP should be kept (with a list of all sources)
Use the LSP-DB version number (similar to RFC8232 - state synchronization optimizations)
  ORIGINAL-LSP-DB-VERSION TLV – which encodes the PCC’s LSP-DB version number (as received from PCC) on the state-sync PCE sessions
  LSP-DB-VERSION TLV is still used with local PCE’s Database version to support state optimization techniques
  A PCE updates the LSP state only if the ORIGINAL-LSP-DB-VERSION present in the PCRpt is greater than the current ORIGINAL-LSP-DB-VERSION of the stored LSP state.
    This ensures that a PCE never tries to update its stored LSP state with an old information.

## Slide 5: Updates in -02: Latest State!
PCE1
PCE2
PCC
State Sync Session
Latest LSP State (V=100)

## Slide 6: Updates in -02: Latest State!
PCE1
PCE2
PCC
State Sync Session
Latest LSP State (V=101)
V=100, ignored

## Slide 7: Updates in -02: Latest State!
PCE1
PCE2
PCC
State Sync Session
Latest LSP State (V=101)
V=101, ignored

## Slide 8: Next Steps
Procedures for the PCE-Initiated LSP need to explicitly stated in the draft.
  Most of the procedure remains same as a delegated LSP
Issue WG adoption call for the Document.
  Problem is worth working on?
  The document is a good foundation.